-------------------------------------------------------------------------------

-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-

" d e f M O N i n g   1 0 2 "

a defMON operator field guide

by iLKke

+ frantic + scannerboy + F7sus4 + Amelinium + FTC + ryba

-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-

-------------------------------------------------------------------------------

disCLAIMER

-------------------------------------------------------------------------------

This guide is the result of my limited defMON knowledge based largely on

experimentation, therefore it almost certainly contains inaccuracies and

omissions. It is not intended as an exhaustive explanation of the program, but

rather a brief survival guide and reference. It assumes basic familiarity with

trackers and the SID chip.

Hope you find this text helpful. You are encouraged to experiment.

-------------------------------------------------------------------------------

intRODUCTION

-------------------------------------------------------------------------------

defMON is what I would call the only true tracker for the C64 (as opposed to

sound 'editors'). No tables with pointers to tables, no multiple lines of table

data performing a single function. In defMON, screen Y-axis is always time, as

in a tracker.

Some advantages of defMON:

-Single, all-powerful instrument table that is easy to read

-No discrimination between instruments & effects (similar to NinjaTracker)

I will refer to these as "sidCalls" in the guide.

-Combine 2 sidCalls at once. This makes it possible to make modifiers for

instruments instead of duplicating and then modifying

-Two cutoff controls so you can modulate/offset a filter envelope

-Relative channel filtering, e.g. filter CURRENT channel

-Most flexible hard restart ever, period. Because you do it all yourself.

You can have each instrument use a completely different HR.

-Almost any SID tune can be remade in defMON (up to 8x speed, and with

the exception of "digis", or samples)

-Adjustable BPM

-Low rastertime use

Some disadvantages of defMON:

-Instruments have no names, you will need to remember some numbers

-You need to manually specify instrument number for each note

-The song packer is built in, but you will need to make a PRG or SID file

yourself

-You might not want to go back

-------------------------------------------------------------------------------

oveRVIEW

-------------------------------------------------------------------------------

defMON consists of 3 screens.

1. The main screen contains the pattern editor on the left (where you put your

notes) and the arranger on the right (where you arrange patterns into a full

song). Each track (channel) has the following columns: sidCALL1,

sidCALL2, note, speed.

Exact order of these columns can differ depending on defMON version.

2. The sidTAB is the only table you will ever need. This is where sounds are

made. It is quite similar to sidDump output. If you know your SID registers you

should have no trouble understanding it.

3. Disk menu is where you load, save and pack your tunes.

-------------------------------------------------------------------------------

keyBOARD REFERENCE

-------------------------------------------------------------------------------

NAVIGATION:

<-		switch pattern/sidTAB

c=+<-		jump to position in sidTAB [pattern]

shift+<-		jump to position in sidTAB [pattern]

ctrl+<-		switch sid1/sid2

runstop		switch pattern/arranger, exit sidTAB

c=+runstop	jump to position in pattern [arranger]

ctrl+curs	step thru patterns (1 step) / sidTAB (8 steps)

ctrl+G/H/J/K	cursor to 0/4/8/C position in pattern

ctrl+GG		cursor to -1 position in pattern

shift+X		disk menu:

return		load song

L		load song

S		save new song

shift+S		overwrite song (!)

shift+P		pack song

space		read dir

W,R		write and read legacy format

</>		prev/next drive

<-		exit

PLAYBACK:

F1		play from cursor

F3		play from start

F5		follow on/off

F7		stop/top

[,],=		mute tracks (Ö,Ä,* on Swedish keyboard)

SETUP:

F2 (shift+F1)	BPM reset (sets speed directly to default value: $4CC7, 1/1)

F2/F4/F6/F8	multispeed (sets speed directly to: $4CC7/$2663/$1331/$0998)

c=+F1		speed + 1 CPU cycle (slower)

c=+F2(shift+F1)	speed - 1 CPU cycle (faster)

c=+F3		speed + 80 CPU cycles (slower)

c=+F4(shift+F3)	speed - 80 CPU cycles (faster)

c=+F5		speed 1/1, 1/2, 1/3, 1/4, 1/5, 1/6, 1/7, 1/8 (slower, 1/1 is default)

c=+F6(shift+F5)	speed 1/8, 1/7, 1/6, 1/5, 1/4, 1/3, 1/2, 1/1 (faster)

c=+F7		speed *2 (slower)

c=+F8(shift+F7)	speed /2 (faster)

ctrl+<,>		octave down/up (shown in right bottom in the main screen)

c=+/		decrease chunksize [sidTAB]

shift+/		increase chunksize [sidTAB]

possible values 0(whole tab),1,2,4,8,$10,$20,$40,$80

INPUT:

return		insert step

shift+return	remove step

<		decrease a value

>		increase a value

shift+N		clone pattern into Next empty pattern [arranger]

shift+U		clone pattern into next pattern that is Unused in the [arranger]

there are 00-7F patterns you can use

c=, shift		edit sidTAB calls (position in sidTAB) [pattern]

If you call two different sidTABs at once and both contains

parameters in the same column (eg. ADSR), the rightmost sidTAB

overwrites the leftmost

ctrl+c=		edit speed column [pattern]

ctrl+c=+SPC	insert pattern break (shown as two red DOTS in sidCALL1 column)

del		delete value

space		delete value+advance step

c=+X		copy row (sidCALLS + Note) [pattern]

c=+V		paste row [pattern]

ctrl+num	edit X steps at once (supER COMMANDS)

FFXXYY	jump to position XX and repeat YY times [arranger]

00 in YY column for infinite repeat

-------------------------------------------------------------------------------

fraMES

-------------------------------------------------------------------------------

sidTAB consists of fraMES (smallest section of time in defMON). Each row represents one fraME

by default. If you increase DL (step delay) by +1, you put one EMPTY fraME (row) after edited

sidTAB step, so it takes 2 fraMES to proceed to another row.

pattern speed column is set to 2 delay steps (DL) by default. This means it takes 2 delayed

(3 actual) fraMES to proceed from one pattern row to another.

-------------------------------------------------------------------------------

sidTAB REFERENCE

-------------------------------------------------------------------------------

SidTAB is running in circle from sidCALL specified in pattern (e.g. 00) to the bottom,

to FF position, than back to 00 and so on, unless it reaches position jump (in JP)

or STop command (in DL) or another sidCALL

Chunks are only aesthetic separations of sidTAB,

When you insert or remove rows, it will only affect the current chunk

JP		position jump

SPC	delete position jump

DL		00-7F	step delay (00-7F fraMES) to advance to next row

80-FF 	insert STop command (execute row and delay forever)

SPC	reset step delay to 00

WG		x0 waveform

+1	triangle

+2	saw

+4	pulse

(you have to set PW - e.g. 08 for 50% square wave)

+8 	noise

WG		0x gate

0	gate off

(executes Release phase of ADSR)

+1	gate on

(executes Attack,Decay,Sustain phase of ADSR)

+2	sync

+4	ringmod

(sync/ringmod is based on channel pairing, 1+2, 2+3, 3+1)

(e.g. used in channel 1 means channel 3 modifies channel 1)

+8	test-bit/reset (resets the oscillator and sets gate to 0)

+9	test bit/reset (resets the oscillator and sets gate to 1)

ADSR		volume envelope (*see below)

TR		transpose (*see table below)

00-7F	relative pitch up (wrap)

(+ 00-7F semitones from basic note - in pattern note column)

80-FF	absolute notes

(value of the basic note in pattern is ignored)

AF		00-19 	finetune (19=note up)

21-7F 	pitch up (wrap)

80-BF 	pitch bend up (wrap)

C0-FF 	pitch bend down (wrap)

PW		pulsewidth set (*see below)

low byte first, then high byte

PS		pulsewidth slide

00-7F	slide left (to 0%, lowering PW value in time)

80-FF	slide right (to 100%, increasing PW value in time)

RE		filter resonance/channel mask

x0	resonance

0x	channel mask

00	disable on current

01	1

02	2

03	1+2

04	3

05	1+3

06	2+3

07	1+2+3

08	current

09	c+1

0A	c+2

0B	c+1+2

0C	c+3

0D	c+1+3

0E	c+2+3

0F	c+1+2+3

FV		filter type

x0	filter type

00,80	off

10,90	lp

20,A0	bp

30,B0	lp+bp (high stop)

40,C0	hp

50,D0	lp+hp (band stop)

60,E0	bp+hp (low stop)

70,F0	lp+bp+hp

CP		relative cutoff offset

00-7F	add

80-FF	substract

ACID		cutoff set/slide

0000-7FFF cutoff set

8000-BFFF cutoff slide up

C000-FFFF cutoff slide down

-------------------------------------------------------------------------------

supER COMMANDS

-------------------------------------------------------------------------------

ctrl+XX 		set XX (00-20) steps to be edited at once

or ctrl+S+XX	(from cursor position to the end of the pattern,

it doesn't work outside of pattern that you're actually in)

ctrl+R+XX	repeat each operation by XX times

ctrl+W+X	set width (0-F), every Xth step will be edited

(1 is default)

ctrl+Z+A	zone all (edit in all 3 patterns or whole sidTAB)

ctrl+return	exit supER COMMANDS mode

_______________________________________________________________________________

supER COMMANDS example

_______________________________________________________________________________

* Clone sequence using the normal SHIFT+N or SHIFT+U operation

* Put cursor on first step of the sequence by pressing CTRL+G twice

* Hold CTRL while typing S 2 0, to put editor in "edit 20 steps at once" mode.

* Transpose the cloned sequence up/down with >/< keys

* Press CTRL+RETURN to get back to normal editing mode again.

If you know for sure that you want to transpose a sequence up 12 ($0C) steps, for example,

you could replace the third step in the procedure with:

* Hold CTRL while typing S 2 0 R C, to put editor in "edit 20 steps at once and repeat

each operation $C times" mode.

Then it will be enough to press > once to transpose the sequence up $0C steps = one octave.

If you want to transpoe ALL notes in the whole song one step up, you could replace the third

step in the procedure with:

* Hold CTRL while typing Z A S 2 0 to put editor in "apply operation to ALL sequences and edit

20 steps at once" mode.

Then pressing > once will transpose every note in the whole song one step up. Obviously this is

a quite dangerous mode to operate in, since accidentally pressing a key will affect the whole song

(e.g. pressing space would erase all notes in the whole song), so make sure to get back to normal

operating mode at once afterwards by pressing CTRL+RETURN.

-------------------------------------------------------------------------------

DinSYNC (scannerboy interface)

-------------------------------------------------------------------------------

ctrl+shift+> 	Midi/Dinsync delay value up

ctrl+shift+<	Midi/Dinsync delay value down

-------------------------------------------------------------------------------

-------------------------------------------------------------------------------

tipS

-------------------------------------------------------------------------------

-------------------------------------------------------------------------------

_______________________________________________________________________________

adsR and gatE BIT

_______________________________________________________________________________

Attack

$0 is quickest and $F is slowest = the time it takes for the volume to rise from zero to max.

The Attack phase starts whenever the GATE bit is turned on (more info on the GATE bit below).

Decay

$0 is quickest and $F is slowest = the time it takes for the volume to fall from max and down

to the Sustain level (see below). The Decay phase starts automatically as soon as the Attack

phase has finished.

Sustain

$0 is silence and $F is the loudest = the VOLUME (not the time) that the ADSR envelope stops

at after having gone through the Attack and the Decay phase. As long as the GATE bit is still on,

the ADSR envelope will stay in the Sustain phase forever. When GATE is turned off, the Sustain

phase ends and the Release phase (see below) starts instead.

Release

$0 is quickest and $f is slowest = the time it takes for the volume to fall from the Sustain level

down to zero volume. More accurately, the Release phase may be started even before the ADSR

envelope has reached the Sustain phase. For example, if you have a really slow Attack, and turn

GATE off before the Attack is done, the Release will start falling from whatever volume the ADSR

is at, rather than from the specified Sustain level.

The GATE bit, that triggers the ADSR, is found in the WG columns on the sidTAB screen in defMON.

Normal usage of the WG columns would be to only use the upper nibble (e.g. the X in $XY) in the

first WG column to set waveforms, and to only use the lower nibble (e.g. the Y in $XY)  in the

second WG column.

So to set triangle waveform (the $10 in the first WG column), and the GATE bit to ON

(the $01 in the second WG column), and ADSR to $11FA, you execute a line that looks like this:

WG WG AD SR

10 01 11 FA

...and then some time later you would execute a line where there is a 00 in the second WG column

to turn the GATE bit off again, which will then have the effect that the ADSR envelope stops

hovering at the Sustain level and instead enters the Release phase. Like this:

WG WG AD SR

.. 00 .. ..

(This is also why there are two WG columns, because it allows the waveform to be "remembered"

(in the first WG column) even if you turn the gate bit off in the second WG column.)

_______________________________________________________________________________

harD RESTART and adsR BUG

_______________________________________________________________________________

The ADSR bug is, more or less, sounds failing to trigger properly because the ADSR envelope

of the previous sound on the same channel didn't clear yet. Sometimes it will drop a note,

sometimes it will make it sound different. This is more noticeable if you're triggering notes

rapidly and also depends a lot on the ADSR values of the sounds involved.

It's worth noting that if you are patient / experienced enough with ADSR values you can avoid

the bug even without using harD RESTART.

For example some people say that setting the Attack to 1 instead of 0 helps, or setting Sustain

to less than F, etc. I just tend to play around.

It still makes the drum sounds punchier.

There are two components to setting up HR, one is resetting the gate bit, and the other

is an ADSR envelope to be set up before the sounds actual envelope, we call this one ADHR.

Also note that there needs to pass some time (2 frames I think) after the HR line before you

trigger the actual sound, thus the wait in the DL column in those examples I posted.

This delay makes the hardrestarted sounds trigger slightly later than the non-HR ones,

so if that is audible in your tune you have to compensate.

With defMON being so flexible you have many options on how to compensate for this delay.

First you can trigger HRed sounds a line in advance (notice how dM has a line before line 0)

or you can set up the sound the line before and then trigger the note later (goto80 does this),

or you could build a little delay into all the non-HR sounds as well, or you could make all your

HRs as separate commands and then trigger those the line before (I use this one when I can).

Again this is only significant if you can hear the unwanted delay.

Or if you need a really rapid fire machinegun beat you can keep the gate open and use other tricks

to mute/control the perceived volume (like setting the waveform to 0 or using really thin pulse widths).

This is more like a kill-switch method so you lose almost all the dynamics, sort of like overcompressing

to death, but it sidesteps the use of ADSR completely and thus the ADSR bug as well.

To round it off, here's some notes I compiled a while ago from CSDb, looking into SID tunes with

siddump, and looking into how different trackers handle it.

dl = delay (in frames)

w = waveform

g = gate bit

ADHR = hard restart envelope

ADSR = envelope for your sound

HARD RESTART

------------

METHODS

old school

dl    w    g    adsr

----------------

1     -    0    0000

0     W    1    ADSR + NOTE

new school

dl    w    g    adsr

----------------

1     -    0    ADHR

0     -    9    ADSR

0     W    1    ---- + NOTE

hybrid

dl    w    g    adsr

----------------

1     -    0    0000

0     -    1    ADSR

0     W    -    ----

heatbeat

dl    w    g    adsr

----------------

0     -    9    ADSR

0     W    1    ---- + NOTE

...

1     -    0    ----

0     -    9    ----

0     W    1    ---- + NOTE

EXAMPLE ADHRs VALUES

0000    hardest

0F00    most common

0F18    Drax

0F20    GRG

0FF0    Randall/Jammer

F000    Linus

FF00    Jeff

OTHER NOTES

Sustain of F is especially buggy (try E then? :)

soft restart usually works best with big (>= 8) release values

_______________________________________________________________________________

-1 steP in pattern

_______________________________________________________________________________

defMON is designed to implement as little "built in" functions as possible.

Things like hardrestart, vibrato, etc...

Instead it is up to the user to do it themselves in the sidTAB.

That comes at a cost of course (less automation), but the benefit is increased flexibility.

You can do any kind of hardrestart in defMON, whereas most other editors only feature one type

of built in hardrestart and no reasonable way to do it manually (especially not at that first

step in the sequence).

Also, implementing hardrestart without that "prior first step" in sequences requires that

the sequence parsing code looks ahead: e.g. that it parses sequences before it is actually

time to parse them, to see if a hardrestart sound is coming up, because the hardrestart has

to be trigged 2-3 fraMES (depending on what sort of hardrestart you do) before the actual

start of the audible sound. Such look ahead-parsing adds overhead to the code and consumes

CPU that isn't strictly required. Original defMON was intended to be usable in demos/games,

with low raster time consumption.

_______________________________________________________________________________

pulSEWIDTH

_______________________________________________________________________________

pulSEWIDTH ranges from $000 to $FFF (from 0% to 100%)

in value of YXY and is set by XY in PW column.

e.g. 83 in PW column sets pulSEWIDTH to 383 value.

Examples:

50% sqare wave ($800) - $F7 ($7F7) and $08 ($808) is closest to ($800)

75% pulse wave ($C00) - $FB ($BFB) and $0C ($C0C) is closest to ($C00)

25% pulse wave ($400) - $F3 ($3F3) and $04 ($404) is closest to ($400)

If pulSEWIDTH is set near to 0% or 100%, the pulse waveform is inaudible.

_______________________________________________________________________________

addITION OF BITS

_______________________________________________________________________________

As for values, they are additive, therefore:

07 = 04 (ringmod) +02 (sync) +01 (gate on)

05 = 04 (ringmod) +01 (gate on)

04 = 04 (ringmod) +00 (gate off)

50 = 40 (pulse, and pulse table applied) + 10 triangle

So basically, $55 may be written as either 5401 or 5005 (in WGWG columns).

_______________________________________________________________________________

_______________________________________________________________________________

-------------------------------------------------------------------------------

traNSPOSE TABLE

-------------------------------------------------------------------------------

relative pitches

0	 	01	02	03	04	05	06	07	08	09	0a	0b

1	0c	0d	0e	0f	10	11	12	13	14	15	16	17

2	18	19	1a	1b	1c	1d	1e	1f	20	21	22	23

3	24	25	26	27	28	29	2a	2b	2c	2d	2e	2f

4	30	31	32	33	34	35	36	37	38	39	3a	3b

5	3c	3d	3e	3f	40	41	42	43	44	45	46	47

6	48	49	4a	4b	4c	4d	4e	4f	50	51	52	53

7	54	55	56	57	58	59	5a	5b	5c	5d	5e	5f

8	60	61	62	63	64	65	66	67	68	69	6a	6b

9	6c	6d	6e	6f	70	71	72	73	74	75	76	77

10	78	79	7a	7b	7c	7d	7e	7f

absolute pitches

C	C#	D	D#	E	F	F#	G	G#	A	A#	B

0		81	82	83	84	85	86	87	88	89	8a	8b

1	8c	8d	8e	8f	90	91	92	93	94	95	96	97

2	98	99	9a	9b	9c	9d	9e	9f	a0	a1	a2	a3

3	a4	a5	a6	a7	a8	a9	aa	ab	ac	ad	ae	af

4	b0	b1	b2	b3	b4	b5	b6	b7	b8	b9	ba	bb

5	bc	bd	be	bf	c0	c1	c2	c3	c4	c5	c6	c7

6	c8	c9	ca	cb	cc	cd	ce	cf	d0	d1	d2	d3

7	d4	d5	d6	d7	d8	d9	da	db	dc	dd	de	df

8	e0	e1	e2	e3	e4	e5	e6	e7	e8	e9	ea	eb

9	ec	ed	ee	ef	f0	f1	f2	f3	f4	f5	f6	f7